## Slide 1
Greenseeker Sensor Development 1989-2015
M.L. Stone, J.B. Solie, and W.R. Raun
Oklahoma State University
TIMELINE
Initial passive sensors developed in 1989 were for detecting and spraying weeds. In 1990, the first order bindweed detector/ sprayer was evaluated. By 1992, engineers and agronomists successfully used NDVI for sensing plant biomass. In 1996, the very first variable N rate applicator was built that could sense and treat every 10 ft2 at 10 mph. By 1998, spring wheat grain yields could be predicted using advanced-passive sensors, CIMMYT, Ciudad Obregon, MX.
OKLAHOMA STATE UNIVERSITY
1989
1992
1996
1998
2001, commercial scale 60 foot applicator could sense and fertilize every 4 ft2 at 15 mph.
2001
In 2002, robust prediction of wheat grain yield potential was possible using climatological data that normalized NDVI.
2002
2007
In 2007, sensing and fertilizing corn, by-plant was possible using Greenseeker sensors and high speed rate controllers
2003
Greenseeker sensor used to collect coefficient of variation (CV) data to better characterize small scale variability and refine fertilizer N rates
In 2008, small scale, more affordable hand held sensor developed, tested and commercialized by Trimble
1995
Accurate prediction of mid-season N rates based on Greenseeker readings, predicated on having an N Rich Strip (1995)
2008
Greenseeker sensors used all over the world
Documenting small scale spatial variability