## Slide 1: Dr. Barbara Stoecker International Nutrition and World Hunger NSCI 5553 326 Human Sciences 4:30 – 6:20 April 8, 2014 http://nue.okstate.edu/Hand_Planter.htm

## Slide 3: Care

## Slide 7: Picture
Importance of photo journalism
Incorporating images/experience
Communication

## Slide 8: World Maize
177,000,000 ha’s in 2012 (FAOstat)
872,000,000 Mg, produced, 4.9 Mg/ha
48,370,000 ha’s in the developing world
60% planted by hand ≈ 29,000,000 hectares or 16% of the total maize area in the world

## Slide 9: 35,000,000 ha’s maize USA (86,000,000 acres corn USA)

## Slide 10: World Maize Production
Global Biogeochemical Cycles 22: GB1022. doi:10.1029/2007GB002947

## Slide 11: 2012, Maize Statistics
 | Area, ha’s |  | Production, Mg | 
World | 177,000,000 |  | 872,066,770 | 
USA | 35,359,790 | 19% | 273,832,130 | 31%
China | 34,966,000 | 19% | 208,234,649 | 24%
Developing (DW) | 48,370,000 | 27% | 97,000,000 | 11%
by hand (60% of DW total) | 29,000,000 | 16% | 58,000,000 | 6%

## Slide 12: Corn Growers Association

## Slide 14: Hand Planter Need
Methods which homogenize maize plant stands and emergence can decrease plant-to-plant variation and increase grain yields (Martin et al., 2005)
Maize emergence delayed by as little as four days, resulted in a yield depression of 15 percent (Hodgen et al., 2007)
Third world maize yields hover near 2.0 Mg/ha (Dowswell, et al., 1996)
“OSU Hand Planter”

## Slide 15
http://nue.okstate.edu/Hand_Planter.htm

## Slide 16
Honduras

## Slide 17
Opico Quezaltepeque, El Salvador

## Slide 18
Zimbabwe

## Slide 19
Dominican Republic

## Slide 20: Alternatives

## Slide 21
Bangladesh
Burundi
Belize
Brazil
Colombia
El Salvador
Ethiopia
Guatemala
India
Kenya
Malawi
http://nue.okstate.edu/Hand_Planter/osu_hand_planter_workshop.html
Mexico
Mozambique
Sierra Leone
Nepal
Philippines
Tanzania
Togo
Uganda
USA
Zambia
Zimbabwe

## Slide 22: http://nue.okstate.edu/Hand_Planter.htm

## Slide 24: Singulation Design

## Slide 25: Reciprocating Drum Action
Drum position when planter is relaxed.
Drum rotates with the cavity moving back into the seed hopper as the spring is compressed.
Spring is fully compressed and the singulation drum cavity is exposed to seed in the hopper
As the force on the spring is released, the singulation drum rotates back to the initial ‘relaxed’ position and the seed is dropped.

## Slide 27: Planter Action
The planter is pressed down and compresses the internal spring.
Singulation drum rotates and seed is released on the down stroke.
The planter is ‘relaxed’ and the spring returns it to the initial position.

## Slide 28
1,000,000 cycles
0.29g/seed
60,000 seeds/ha
3443 seeds/kg
1.0 kg hopper
17 times refill
seed size (2653-4344 seeds/kg) seed type, shape
fertilizer
http://nue.okstate.edu/Hand_Planter.htm

## Slide 29
Dr. Randy Taylor
Dr. Nyle Wollenhaupt
1,000,000 cycles, no failures 1 hectare, 100,000 seeds/ha, 10 years

## Slide 30: Importance of Singulation
0.76m Row Spacing
Heterogeneity in plant spacing, and plant stands reduce yields (1997, Nielsen, Purdue)

## Slide 31
Chart: Housing, Brush, Drum, Seed Size
| H1st 450s 3572 | H1st 450s 3263 | H1st 450s 2652 | H1st 450b 3572 | H1st 450b 3263 | H1st 450b 2652 | H1so 450s 3572 | H1so 450s 3263 | H1so 450s 2652 | H1so 450b 3572 | H1so 450b 3263 | H1so 450b 2652 | check 3263
Singles | 65 | 63.3333 | 75 | 55 | 55 | 70 | 78.3333 | 85 | 85 | 71.6667 | 80 | 86.6667 | 98.3333
Doubles | 31.6667 | 28.3333 | 16.6667 | 38.3333 | 43.3333 | 26.6667 | 8.3333 | 8.3333 | 3.3333 | 21.6667 | 16.6667 | 5 | 0
Nov 13, 2013
SED = 8.6

## Slide 33: Rotating Drum
Drum | Mass (g) | Volume (cm3)
A | 0.69 | 0.507
B | 0.71 | 0.521
OS | 0.88 | 0.646
OM | 3.36 | 2.468
OC | 3.38 | 2.482

## Slide 34: Mid Season Fertilizer N
Combined, Efaw and Perkins, 2013 |  | 
Topdress N, Corn, V12 |  | (70,000 s/ha)
Methods | N, kg/ha | Mg/ha
Check | 0 | 6.6
Hand planter (0.9 g/plant) | 30 | 11.2
Hand planter (1.8 g/plant) | 60 | 10.6
Broadcast | 30 | 6.4
Broadcast | 60 | 7.0
Dribble urea | 30 | 9.3
Dribble urea | 60 | 7.8
Dribble UAN | 30 | 7.3
Dribble UAN | 60 | 10.4
SED = 1.81 |  | 

## Slide 36
Thailand Mexico Zambia El Salvador Guatemala
Regional Trials: El Salvador, Thailand, Colombia, Uganda, Zambia

## Slide 37: Variables
Brush size, location, stiffness
Drum orientation
Drum cavity size
Drum angle
Internal Housing (1, 2, 3) (brush position)
Seed size, shape (range from 2652 to 4344 seeds/kg)
Operator (many)

## Slide 38
Benefits
Remove chemically treated seeds from the hands of small farmers
Decrease soil erosion via improved plant spacing
Accommodate mid-season application of urea-N
Place urea below the surface reducing NH3 losses
Potential to increase maize production and NUE

## Slide 40: Latitude
“The human mind, when stretched by a new idea, can never shrink to its original size” Oliver Wendell Holmes

## Slide 41
By 2050 there will be 9.1 billion people.
Increase of 30%
Food production during the same period will have to increase 70%
95% of the increased population will be in the developing world

## Slide 42
Food and Agricultural Organization, “Livestock's Long Shadow” surveys damage done by sheep, chickens, pigs and goats. But in almost every case, the world's 1.5 billion cattle are most to blame. Livestock are responsible for 18 per cent of the greenhouse gases that cause global warming, more than cars, planes and all other forms of transport put together.
The Independent.co.uk
Agriculture and the Environment

## Slide 43
Of the 7 billion people in the World, more than 1 billion live on less than $1 per day.
More than 2.7 billion live on less than $2 per day.

## Slide 44
Grain production is vital because worldwide people get 48% of their calories from eating grain directly. As incomes rise, the percent drops dramatically as diets change to include more meat, milk, eggs and other foods that require more grain to produce. About 48% of grains are eaten directly, 35% fed to animals, and 17% for ethanol and other fuels.
Worldwatch Institute, August 12, 2011 worldwatch.org