## Slide 1
Bill Raun, Randy Taylor, Nyle Wollenhaupt, Bruno Figueiredo, Lawrence Aula, Joshua Ringer, Edgar Ascencio, Jagmandeep Dhillon
Hand Planter for Emerging Countries
Global Horticulture
Dr. Mike Schnelle

## Slide 2: Hand Planters
Person | Organization | Where | No. of Hand Planters
Dr. Isaiah Nyagumbo | CIMMYT, Kenya | Zimbabwe | 4
Dr. Pascal Kaumbutho | KENDAT, Kenya | Kenya | 2
 | Ethiopia | Ethiopia | 1
Dr. Peter Omara | Uganda | Uganda | 3
Dr. Edgar Ascencio | CARE, El Savador | El Salvador | 4
Dr. Fred Kanampiu | IITA, Kenya | Kenya | 2
Dr. Nyle Wollenhaupt | AGCO, Kansas | Kansas | 2
Dr. Ivan Ortiz-Monasterio | CIMMYT, Mexico | Mexico | 1
Kristin Lacy | Semilla Nueva | Guatemala | 2
Nyle Wollenhaupt | AGCO | Lusaka Zambia | 40
Melvin Siwale | AGCO | Lusaka Zambia | 10
Terry Tindall | JR Simplot | Lusaka Zambia | 25
Eric Lam | MAG | Honduras | 2
Eric Lam | CIMMYT | Bangladesh | 1
Dr. Luis Narro | CIAT | Colombia | 1
Dr. Joshua Ringer |  | Thailand | 1
Dr. Assoumane Maiga |  | Mali | 1
Total |  |  | 101
Notes: 2

## Slide 3: Borlaug: Volume 3, Bread Winner. 1960-1969. Copyright 2004, 2010 by Noel Vietmeyer
…But the technology package was only one aspect. Once we had the package and had checked it for its validity, we still had to harness it to political policies. Otherwise, nothing would have happened and the technology, as good as it was, would never have been applied and food production would have stayed unchanged. We had to see that the credit was available for small farmers to buy the inputs needed to obtain these yields. We also had to see that pricing at the time of harvest was enough to stimulate farmers to adopt this package.
“Then, can man use honest work, God’s best medicine to gain his own livelihood.”
Norman E. Borlaug
“You can’t get him to admit he’s got a Nobel Prize, any other award (he has hundreds), honorary degrees (dozens), or that he’s helped anyone (millions, if not billions).” Noel Vietmeyer

## Slide 4: Maize (FAOSTAT, 2013)
Area, ha Production, Mt Avg. Mt/ha
World 184,239,959 1,016,431,783 5.5 (87 bu/ac)
USA 35,478,012 353,699,441 9.9 (157 bu/ac)
China 35,276,500 217,830,000 6.2 (98 bu/ac)
Brazil 15,450,180 80,516,571 5.2 (83 bu/ac)
Low income Food Deficit Countries
49,356,985 117,590,512 2.4 (38 bu/ac)
60% hand planted
29,614,180
USA 2014, 37,125,000 ha’s

## Slide 5
World area planted by hand ≈ corn area in the USA
Developing world, avg. farm size = 1 ha
NGO support, interaction, source for subsidizing planters
By 2050 there will be 9.1 billion people.
Increase of 30%
Food production during the same period will have to increase 70%
95% of the increased population will be in the developing world
Alexandratos, N. and J. Bruinsma. 2012. World agriculture towards 2030/2050: the 2012 revision. ESA Working paper No. 12-03. Rome, FAO.

## Slide 7
EL SALVADOR

## Slide 8
ZIMBABWE

## Slide 9
HONDURAS

## Slide 10: Singulation Design

## Slide 11: Reciprocating Drum Action
Drum position when planter is relaxed.
Drum rotates with the cavity moving back into the seed hopper as the spring is compressed.
Spring is fully compressed and the singulation drum cavity is exposed to seed in the hopper
As the force on the spring is released, the singulation drum rotates back to the initial ‘relaxed’ position and the seed is dropped.

## Slide 12
1,000,000 cycles
0.29g/seed
60,000 seeds/ha
3443 seeds/kg
1.0 kg hopper
17 times refill
seed size (2653-4344 seeds/kg) seed type, shape
fertilizer
http://nue.okstate.edu/Hand_Planter.htm

## Slide 13: INTERNAL DRUM
Drum | Mass (g) | Volume (cm3)
A | 0.69 | 0.507
B | 0.71 | 0.521
OS | 0.88 | 0.646
OM | 3.36 | 2.468
OC | 3.38 | 2.482

## Slide 15
OSU Hand Planter

## Slide 16: Mid Season Fertilizer N
Combined, Efaw and Perkins, 2013 |  | 
Topdress N, Corn, V12 |  | 70,000 plants/ha
Methods | N, kg/ha | Mg/ha
Check | 0 | 6.6
Hand planter (0.9 g/plant) | 30 | 11.2
Hand planter (1.8 g/plant) | 60 | 10.6
Broadcast | 30 | 6.4
Broadcast | 60 | 7.0
Dribble urea | 30 | 9.3
Dribble urea | 60 | 7.8
Dribble UAN | 30 | 7.3
Dribble UAN | 60 | 10.4
SED = 1.81 |  | 

## Slide 17: Importance of Singulation
0.76m Row Spacing
Heterogeneity in plant spacing, and plant stands reduce yields (Bob Nielsen, http://www.agry.purdue.edu/ext/corn/pubs/agry9101.htm)

## Slide 18
Chart: Housing, Brush, Drum, Seed Size
| H1st 450s 3572 | H1st 450s 3263 | H1st 450s 2652 | H1st 450b 3572 | H1st 450b 3263 | H1st 450b 2652 | H1so 450s 3572 | H1so 450s 3263 | H1so 450s 2652 | H1so 450b 3572 | H1so 450b 3263 | H1so 450b 2652 | check 3263
Singles | 65 | 63.3333 | 75 | 55 | 55 | 70 | 78.3333 | 85 | 85 | 71.6667 | 80 | 86.6667 | 98.3333
Doubles | 31.6667 | 28.3333 | 16.6667 | 38.3333 | 43.3333 | 26.6667 | 8.3333 | 8.3333 | 3.3333 | 21.6667 | 16.6667 | 5 | 0
Nov 13, 2013
SED = 8.6

## Slide 19
1,000,000 cycles, no failures 1 hectare, 100,000 seeds/ha, 10 years

## Slide 20: UGANDA

## Slide 21
El Salvador, Hand Planter Trials, June, 2014

## Slide 24
Thailand Mexico Zambia El Salvador Guatemala
OSU Hand Planter

## Slide 25
Benefits
Remove chemically treated seeds from the hands of small farmers
Decrease soil erosion via improved plant spacing
Accommodate mid-season application of urea-N
Place urea below the surface reducing NH3 losses
Potential to increase maize production and NUE
Khim et al. (2014). Over three sites, planting 1 seed, every 0.16m increased yields by an average of 1.15 Mg ha-1 (range, 0.33 to 2.46 Mg ha-1) when compared to the farmer practice of placing 2 to 3 seeds per hill, every 0.48 cm.

## Slide 26
GUATEMALA

## Slide 27
GreenSeeder Manual
http://www.nue.okstate.edu/Hand_Planter/Planter%20User's%20Manual%20EL.pdf

## Slide 28
Bangladesh
Burundi
Belize
Brazil
Colombia
El Salvador
Ethiopia
Guatemala
India
Kenya
Malawi Mali
January 2014, on-line hand planter workshop http://nue.okstate.edu/Hand_Planter/osu_hand_planter_workshop.html
Mexico
Mozambique
Sierra Leone
Nepal
Philippines
Tanzania
Togo
Uganda
USA
Zambia
Zimbabwe

## Slide 29
“The most conservative man in traditional agriculture is the scientist, and sometimes I am not proud to be one of them. This is most discouraging. The scientist is a privileged person, the man should lead us out of the wilderness of static, underproductive agriculture, and yet by his apathy and failure to exercise his unique vision, he keeps us in the swamp of despair. The scientist fears change because he is in a relatively privileged position in his own society. If there is no breakthrough in yield, he will not be criticized. But if he makes a recommendation and something goes wrong, he may lose his job. “ N.E. Borlaug