## Slide 1
Origin, Development and Delivery of the OSU Hand Planter Wednesday, September 2, 2020 11:30 am AGIN 5312 Dr. Shida Henneberry, MIAP Mikayla Lin Dolch
nue.okstate.edu

## Slide 2
Minden, Nebraska, 1957-1959 Mexico City, Mexico, 1960-1963 Bogota, Colombia, 1964-1967 Cali, Colombia, 1968-1974
Oklahoma State University, 1975-1982 University of Nebraska, 1982-1985 CIMMYT, Mexico, Guatemala, 1985-1991 Oklahoma State University, 1991-present
CaSO4 DAP, 3-17
Volcan de fuego
Middle America

## Slide 3
1892
Free living cyanobacteria (blue green algae) found in the check plot.
Sun, et al., 2004. Bacterial community structure and diversity in a century-old manure-treated agroecosystem. Appl. Environ. Micro. 70:5868-5874.

## Slide 4
Wheat Fertility Experiment No.502
North Central Experiment Station Established 1970
Plot size: 16’ x 60’
Alley: 20’
Total Trial Area: 224’ x 300’
TRT | Pre-plant N rate (lb N / ac) | Pre-plant P rate (lb P2O5 / ac) | Pre-plant K rate (lb K2O / ac)
1.* | 0 | 0 | 0
2.* | 0 | 40 | 60
3.* | 20 | 40 | 60
4.* | 40 | 40 | 60
5.* | 60 | 40 | 60
6.* | 80 | 40 | 60
7.* | 100 | 40 | 60
8. | 60 | 0 | 60
9. | 60 | 20 | 60
10. | 60 | 60 | 60
11. | 60 | 80 | 60
12. | 60 | 60 | 0
13. | 100 | 80 | 60
14. | 60 | 40 | 60 (Sul-Po-Mag)
N applied as 46-0-0 (Urea) P applied as 0-46-0 (Triple Super Phosphate) K applied as 0-0-60 (Potash) * - YP plot |  |  | 
S
W
N
E
Location: Lahoma
 | 300 | 4 | 5 | 12 | 13 | 20 | 21 | 28 | 29 | 36 | 37 | 44 | 45 | 52 | 53
Rep 4 |  | 3 | 5 | 13 | 6 | 10 | 2 | 4 | 7 | 12 | 1 | 8 | 14 | 9 | 11
 | 240 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56
 | 220 | 3 | 6 | 11 | 14 | 19 | 22 | 27 | 30 | 35 | 38 | 43 | 46 | 51 | 54
Rep 3 |  | 1 | 14 | 2 | 7 | 11 | 3 | 9 | 12 | 5 | 13 | 4 | 8 | 10 | 6
 | 160 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42
 | 140 | 2 | 7 | 10 | 15 | 18 | 23 | 26 | 31 | 34 | 39 | 42 | 47 | 50 | 55
Rep 2 |  | 4 | 8 | 3 | 1 | 11 | 13 | 12 | 7 | 14 | 6 | 9 | 10 | 2 | 5
 | 80 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | 60 | 1 | 8 | 9 | 16 | 17 | 24 | 25 | 32 | 33 | 40 | 41 | 48 | 49 | 56
Rep 1 |  | 8 | 2 | 4 | 6 | 14 | 9 | 10 | 5 | 7 | 12 | 1 | 3 | 13 | 11
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
 | 0 | 16 | 32 | 48 | 64 | 80 | 96 | 112 | 128 | 144 | 160 | 176 | 192 | 208 | 224
1, 2 – Harvest Sequence Number
1, 2 – Treatment Number
1 , 2 – Soil Sample Sequence Number
OBJECTIVE: To study fertilizer nitrogen, phosphorus, and potassium in winter wheat. In recent years, this study has also been used to develop yield potential models and yield predictions through sensor based technologies.
Grant silt loam (fine-silty, mixed, superactive, thermic, Udic Argiustoll
1970

## Slide 6
Wheat Fertility Experiment No.222
Agronomy Research Station Established 1969
Plot size: 20’ x 60’
Alley: 17’
Total Trial Area: 137’ x 520’
TRT | Pre-plant N rate (lb N / ac) | Pre-plant P rate (lb P2O5 / ac) | Pre-plant K rate (lb K2O / ac)
1.* | 0 | 60 | 40
2.* | 40 | 60 | 40
3.* | 80 | 60 | 40
4.* | 120 ^ | 60 | 40
5. | 80 | 0 | 40
6. | 80 | 30 | 40
7. | 80 | 90 | 40
8. | 80 | 60 | 0
9. | 80 | 60 | 80
10.* | 0 | 0 | 0
11. | 120 ^ | 90 | 80
12. | 120 ^ | 90 | 0
13. | 80 | 60 | 40 (Sul-Po-Mag)
N applied as 46-0-0 (Urea) P applied as 0-46-0 (Triple Super Phosphate) K applied as 0-0-60 (Potash) * - YP plot ^ - Split 120 lb N rates to 60 lb N (fall) and 60 lb N (spring) |  |  | 
N
E
S
W
Location: Stillwater
1, 2 – Harvest Sequence Number
1, 2 – Treatment Number
1 , 2 – Soil Sample Sequence Number
OBJECTIVE: To study fertilizer nitrogen, phosphorus, and potassium in winter wheat. In recent years, this study has also been used to develop yield potential models and yield predictions through sensor based technologies.
137 | 52 | 49 | 48 | 45 | 44 | 41 | 40 | 37 | 36 | 33 | 32 | 29 | 28 | 25 | 24 | 21 | 20 | 17 | 16 | 13 | 12 | 9 | 8 | 5 | 4 | 1
 | 13 | 13 | 8 | 5 | 7 | 3 | 2 | 11 | 12 | 6 | 9 | 1 | 10 | 4 | 6 | 2 | 11 | 5 | 3 | 8 | 12 | 10 | 9 | 1 | 7 | 4
77 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | Rep 2 | Rep 1 | Rep 2 |  |  |  |  |  |  |  |  |  |  |  | Rep 1 |  |  |  |  |  |  |  |  |  |  | 
60 | 51 | 50 | 47 | 46 | 43 | 42 | 39 | 38 | 35 | 34 | 31 | 30 | 27 | 26 | 23 | 22 | 19 | 18 | 15 | 14 | 11 | 10 | 7 | 6 | 3 | 2
 | 13 | 13 | 8 | 10 | 7 | 12 | 9 | 5 | 2 | 11 | 1 | 3 | 4 | 6 | 3 | 11 | 1 | 8 | 6 | 9 | 12 | 2 | 5 | 10 | 4 | 7
0 | 52 | 51 | 50 | 49 | 48 | 47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32 | 31 | 30 | 29 | 28 | 27
 | Rep 4 | Rep 3 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 260 | 280 | 300 | 320 | 340 | 360 | 380 | 400 | 420 | 440 | 460 | 480 | 500 | 520
 |  |  | Rep 4 |  |  |  |  |  |  |  |  |  |  |  | Rep 3 |  |  |  |  |  |  |  |  |  |  | 
Kirkland silt loam (fine, mixed, thermic, Udertic Paleustoll
1969

## Slide 7
E222

## Slide 8
Planter Chronology (35 years) 1985, CIMMYT
1987, Regional Agronomist Central America
1991, Faculty OSU
1999, FP - Hand Planter work
2000, Design/construction started
2013, OSU-MS, Aula, Omara
2019, Planter redesign, Rotary Grant / Importance
Rotary Contributions (OK, NE, Nigeria)

## Slide 11
1987 (33)

## Slide 15
ZIMBABWE, UGANDA
Remote Locations Surface applications of urea

## Slide 16
Internal Brush/Strength
Drum size/material
Cavity size/angle
Tip size/design/material
Internal/Ext. spring/tension

## Slide 17
Singulation Design 3D printing
Rotary International AGCO Sitlington Chair
ASA Reinvest, Jessica Davis
Tolerances
Materials
Failure analysis/testing

## Slide 20
Wayne Kiner
Koemel Law, PLLC 205 W. 7th Ave. Suite 101-B Stillwater, OK 74074
http://nue.okstate.edu/Hand_Planter.htm
Kearney County Fair Minden, Nebraska
Randy Taylor tolerance testing
Institutional Memory

## Slide 21
Wayne Kiner, Mandela Fellows 2018

## Slide 22
Current Cost Estimates
Grand Victory Ltd Tsim Sha Tsui Hong Kong Rm 1604 16/F Lee Wai Coml Bldg Tsim Sha Tsui
1000, $25 each
Usman Ali, Nigeria, Mandela Fellows
July 11, 2019: Bernard Ato Brown , Kumasi Ghana (Agricultural Engineer)

## Slide 23
Social aspects/technology transfer
EL SALVADOR
Opico Quezaltepeque, El Salvador
LIRA UGANDA
Worlds Apart
Avg. Farm Size: 1 ha
Avg. Maize Grain Yield, 2 Mg/ha Maize seed, Hybrids (US, others)
Peter Omara MS 2013

## Slide 24
Importance of Singulation
0.76m Row Spacing
Heterogeneity in plant spacing, and plant stands reduce yields
www.agry.purdue.edu/ext/corn/pubs/agry9101.htm

## Slide 25: Homogeneity of plant stands

## Slide 26
Combined, Efaw and Perkins |  | 
Topdress N, Corn, V12 |  | 70,000 plants/ha
Methods | N, kg/ha | Mg/ha
Check | 0 | 6.6
Hand planter (0.9 g/plant) | 30 | 11.2
Hand planter (1.8 g/plant) | 60 | 10.6
Broadcast | 30 | 6.4
Broadcast | 60 | 7.0
Dribble urea | 30 | 9.3
Dribble urea | 60 | 7.8
Dribble UAN | 30 | 7.3
Dribble UAN | 60 | 10.4
SED = 1.81 |  | 
MID Season Fertilizer N

## Slide 27
Benefits
Remove chemically treated seeds from the hands of producers
Decrease soil erosion via improved plant spacing
Accommodate mid-season N application
Urea placed below the surface reducing NH3 loss
Increased production and NUE
Potential Uses
Seed, all types
Alternative chemicals, EPA, mosquito abatement
Food plots/hunters
Gardeners

## Slide 28
$
NOT DONE YET

## Slide 29
MAIZE (FAOSTAT.COM)
Area, ha Production, Mt Avg. Mg/ha
World 183,319,737 1,038,281,035 5.7 (90 bu/ac)
USA 33,644,310 361,091,140 10.9 (174 bu/ac)
China 35,981,005 215,812,100 6.2 (98 bu/ac)
Brazil 15,450,180 80,516,571 5.2 (83 bu/ac)

## Slide 30
Dr. Robert L. Westerman
Opportunity
Professor R.A. Olson

## Slide 31
Norman Borlaug Mother Teresa 1914 – 2009 1910 - 1997

## Slide 33
Coffee Coffea arabica
Rubber Hevea brasiliensis, 1940 USDA
2500-6000 ft asl
Hemileia vastatrix, leaf rust
(more at lower altitudes)
Coffee Imports to the US (2019)
Colombia $1.14 B
Brazil $1.03 B
Vietnam $300 M
Guatemala $320 M
Indonesia $280 M
Honduras $297 M
Nicaragua $295 M
Costa Rica $140 M
Mexico $160 M

## Slide 34
13.3 million acres of corn IA
9.5 million acres of corn NE (200 bu/ac irrigated, 147 bu/ac dryland)
7.6 million acres of wheat, KS (48 bu/ac) 2017
5.3 million acres of wheat, OK (39 bu/ac) 2015
1.0 million acres of wheat, NE, (46 bu/ac) 2017
5.7 million acres of soybeans, NE (58 bu/ac) 2017
12.6 million cattle (cows + CAFO’s Texas)
6.6 million cattle (cows + CAFO’s Nebraska)
5.1 million cattle (cows + CAFO’s Oklahoma)
John Deere invented the steel plow in 1837, Barbed wire 1874, extensive tillage/first tractor, 1892 (John Froelich, Clayton County IA) Atmospheric CO2, 1880 (290 ppm) Atmospheric CO2, 2010 (407 ppm) Atmospheric CO2, 2016 (411 ppm) Atmospheric CO2, 2020 (414 ppm)
Animal agriculture accounts for 18% of all GHG emissions (CO2 equivalent, CH4=20x that of CO2, N2O=300x that of CO2)
Tillage 1890 forward, responsible for 25% of the CO2 increase
Population Nebraska 1.92
Kansas 2.78
Iowa 3.03
Oklahoma 3.93

## Slide 36
Frontier Rotary, Stillwater Oklahoma Stillwater Centennial, Stillwater, Oklahoma Mustang Rotary, Mustang, Oklahoma Minden Rotary, Minden, Nebraska Kearney Rotary, Kearney, Nebraska
District 5750, Oklahoma
District 5630, Nebraska
District 9125, Nigeria

## Slide 37
Time, $, Products
post PhD, 1985-present, 34 years
Greenseeker Years: 1991–2001, 11 years, $4.7M
Delivery, 2002-present
Stone, Solie, students
OSU Hand Planter (Greenseeder)
Years: 1987-2020, 33 years, $175K
Taylor, Koller, many students,
  Delivery, >450, plans for more
OSU graduates, Kenya, Uganda, El Salvador, Mexico, Dr. Joshua Ringer, Dr. Craig Edwards, Mandela Washington Fellows