## Slide 1: Impressions of China and More
Dr. Chuanguo Xu

## Slide 2
Dr. Fang Chen
Regional Director IPNI
Mr. Maury Keonig
Vice-President Ag Services

## Slide 3
What Do You Want from Us ?
“Tell us about recent in-season N management technologies and strategies AND how to effectively convey management information to farmers”
Xu, Chuanguo
Where to Start ?

## Slide 4
Near Infrared
Wavebands
(NIR)
Photosynthesis
Biomass
e l d
Chlorophyll captures BLUE and RED light
Sensors Measure
● Disappearance of red light
● Abundance of reflected NIR
Reflects NIR
Visible
Wavebands
Chlorophyll

## Slide 5
Near Infrared
Wavebands
(NIR)
Photosynthesis
Chlorophyll Biomass
“VIGOR”
Nutrient Status
Y i e l d
Vegetation Index
Visible
Wavebands

## Slide 6
Modulation/Demodulation Using Polychromatic LEDs
LED
PD1
TARGET
SENSOR
PD2
User Selected
Filters
ACS-470
PD3
Features
Select 3 wavebands
Mapping
External GPS
External power
Waveband output
Output to data logger
Continuous data (10 Hz)
Real-time applications

## Slide 7
Crop Circle ACS-430
or
AgLeader OptRx
Cotton
Greece - 2010

## Slide 8
Instrumentation in Chinese Laboratory
ASD sensor (hyper-spectral)
CropSCAN sensor (16 wavebands)
Minolta SPAD meters
Li-Cor light bar
EM 38 (map electrical conductivity)
Trimble DGPS
Hach portable chemistry kit (pH, EC, more)
Canister-type passive sensors (up and down)
Wave-band specific sensors (Chinese built)
Spectralon reference panels (several)
Grey-scale calibration panels (several sets of 4)
GreenSeeker
Circuit boards being developed and tested

## Slide 9
Modulation/Demodulation Using Polychromatic LEDs
LED
PD1
TARGET
SENSOR
PD2
Red, Red-edge and
NIR Filters
RapidSCAN
PD3
Built-In
GPS
Lithium battery
Waveband output
3 Meg memory
Averages data @ 10 Hz
Statistics
Start – Stop switch
Collects data @ 40,000 Hz

## Slide 10
Near Infrared
Wavebands
(NIR)
Photosynthesis
Chlorophyll Biomass
Vegetation Index
Visible
Wavebands
Affected By :
Growth stage
Cultivar (variety)
Previous crop
Water stress
Soil properties

## Slide 11
“ X “
Reference
Sufficiency Index
“Happy Crop”
“Managed Crop”
Note : Reference value - - - remains constant
=
=
S I
Relative “Vigor”
(i.e., 92% adequate)
i.e., 100%

## Slide 12
Chart: Histogram

## Slide 13
Chart: Histogram

## Slide 14
Chart: Histogram
4.47
5.21
SI =
= 0.85

## Slide 15
Holland K.H. and J.S. Schepers. 2010. Derivation of a variable rate nitrogen application model for in-season fertilization of corn. Agronomy Journal 102:1415-1424.
Basic Algorithm
Nappl = ( Nopt – Ncred )
√
√
(1 – SI)
∆ SI
Farmer Rate
or NEONR

## Slide 16
Chart: Sufficiency Index
| 0.54900000000000004 | 0.70899999999999996 | 0.81799999999999995 | 0.82599999999999996 | 0.876
V9 | 0.377 | 0.71 | 0.951 | 0.927 | 1
V12 | 0.377 | 0.71 | 0.951 | 0.927 | 1
Chart: N Rate (kg/ha)
| 0 | 50 | 100 | 150 | 200
 | 0.549 | 0.709 | 0.818 | 0.826 | 0.876
Fertilizer N Rates influence crop vigor
(sufficiency index)
Crop Sufficiency Index is directly related to Relative Yield

## Slide 17
Why Some Precision Agriculture Tools Have Slow Adoption ?
Time
Expense
Intimidated by the technology
Inconvenient
Lack of support after the sale
Not appropriate for the situation
Profits are already adequate
Requires different equipment
Needs technical assistance and guidance

## Slide 18
Producer Services
Grid soil samples
Review yield maps
Generate zone maps for VRT
VRT fertilizer and lime
Check preplant uniformity and deliver materials
Check and calibrate starter fertilizer equipment
Planter uniformity and depth
Sidedress nutrient deliveries
Herbicide applications (high clearance sprayers)
Calibrate fertigation pumps and schedule applications
Field scouting (irrigation, weeds, insects, disease)
Remote sensing (color imagery out the window)
Yield monitor calibration
Help clean up yield maps
Smoke Test
Frequent contacts
Demonstrates concern
Near real-time feedback
Charges 5-7% more
for products

## Slide 19
Excess N
Problems
Appropriate Early-Season N
Courtesy: Fred Below

## Slide 20
Should we be working to -
build a better mouse trap ?
OR
Convincing farmers that they should try to -
catch the mouse ?
Get Involved with Producers

## Slide 21
Thank You
Jim Schepers
402-310-6150
james.schepers@gmail.com