## Slide 1: Comparison of Active Optical Sensors
Ray Asebedo and Dave Mengel
Kansas State University

## Slide 2: Previous work
K-State has had sensor based N rate algorithms available for use with the GreenSeeker and CropCircle sensors since 2009, for wheat and grain sorghum.
The wheat algorithms were revised and expanded as to single topdress or intensive N management versions in 2013.
These algorithms seem to work successfully with the GreenSeeker and Crop Circle sensors.

## Slide 3: KSU Sensor Research and Development
Focus on developing Nitrogen fertilizer Recommendation and yield estimation models for corn, wheat and grain sorghum.
Models are for use state wide, over a wide range of growth stages, climatic conditions, cropping systems and variable field conditions.
Currently available algorithms and those under construction are not made specifically for one brand of sensor, but for all active light source sensors that use Red NDVI.

## Slide 4: Basic questions
Do we need to develop specific algorithms for each of the sensors currently available when using sensors on corn?
Can we develop calibrations for a variety of sensors in order to normalize the data and allow our algorithms to be used with multiple brands and models of sensors?
Can any Red NDVI sensor work with the KSU algorithms with the accuracy and precision we intended?

## Slide 5: Sensor Comparison Topics
Height Sensitivity
Speed Sensitivity
Signal to Noise
Correlation of Red NDVI across sensors

## Slide 6: Experiment Design
7 Corn sites in 2013
Plot size 10 feet wide by 50 feet long
0 to 220 lbs N/ac applied in single and split applications at preplant, V6, V10, and R1.
Treatments arranged in an RCBD with 4 replications
Plant populations ranged from 17000 plts/ac to 33000 plts/ac

## Slide 7: Sensors Utilized and Methods
Trimble Greenseeker 2
Trimble Greenseeker HandHeld (pocket sensor)
Holland Scientific Crop Circle ACS-470
Holland Scientific Rapid Scan (obtained late)
  Ground Speed 3 fps (walking)
  Height 36 inches above canopy

## Slide 8: Basic Sensor Differences
Trimble Greenseeker 2
  Uses Red 660 nm and NIR 770 nm
  Sensor to Canopy Range: 24 to 60 inches
  Sampling rate 20 hz
Trimble Greenseeker Handheld
  Uses Red 660 nm and NIR 770 nm
  Sensor to Canopy Range: 24 to 48 inches
  Sampling rate 2 hz
  Pulse Modulation

## Slide 9: Basic Sensor Differences
Holland Scientific Rapid Scan
  Red 670 nm and NIR 780 nm
  Sensor to Canopy Range: 12 to 118 inches
  Sampling Rate : 12 hz
Holland Scientific ACS-470
  Red 670 nm and NIR 760 nm
  Sensor to Canopy Range: 22 to 60 inches
  Sampling Rate : 10 hz

## Slide 10
Rapid Scan Above
Greenseeker Handheld Below
ACS-470 Above
Greenseeker 2 Below

## Slide 11: 2013 Corn V6 through R1
Chart: ACS-470 vs Greenseeker 2

## Slide 12: 2013 Corn V6 through R1
Chart: ACS-470 vs Rapid Scan
Chart: ACS-470 vs Greenseeker HH

## Slide 13: 2013 Corn V6 through R1
Chart: Greenseeker 2 vs Greenseeker HH
Chart: Greenseeker 2 vs Rapid Scan

## Slide 14: Initial Summary
Greenseeker 2 and ACS-470 provide similar data throughout the growing season.
Rapid Scan and Greenseeker Handheld also correlate well with the Greenseeker 2 and ACS-470.
  The NDVI values from the handhelds are slightly higher.
  Appears to be more variability in the data from the handhelds.

## Slide 15: Site Specific
Chart: Sterling Corn V10 17000 Plants/Acre
| 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216
ACS-470 | 0.63416 | 0.67517 | 0.6911 | 0.58443 | 0.73339 | 0.65206 | 0.67032 | 0.68211 | 0.68186 | 0.6846 | 0.73041 | 0.64997 | 0.72771 | 0.64829 | 0.71731 | 0.61401
Greenseeker 2 | 0.61982 | 0.67436 | 0.68122 | 0.58597 | 0.72717 | 0.65082 | 0.64413 | 0.6824 | 0.66818 | 0.68321 | 0.71303 | 0.65435 | 0.7232 | 0.66092 | 0.70674 | 0.60432
Greenseeker Handheld | 0.72 | 0.75 | 0.74 | 0.69 | 0.76 | 0.72 | 0.71 | 0.72 | 0.74 | 0.75 | 0.77 | 0.72 | 0.78 | 0.73 | 0.77 | 0.68
Rapid Scan | 0.7066 | 0.7647 | 0.7529 | 0.6791 | 0.781 | 0.7166 | 0.7317 | 0.7561 | 0.7327 | 0.7524 | 0.7747 | 0.7352 | 0.7718 | 0.7304 | 0.7736 | 0.6792
All of the sensors follow the same trends. The amount of observed NDVI change is less in the handheld sensors. Lower plant population, erect leaf architecture, sensor footprint and sampling rate are potential reasons.

## Slide 16: Sterling Corn V10

## Slide 17
Chart: Sterling Corn V10 Nitrogen Recommendations
| 201 | 204 | 207 | 209 | 216
ACS-470 | 79 | 97 | 60 | 54 | 87
Rapid Scan | 63 | 76 | 52 | 52 | 76
Greenseeker Handheld | 47 | 64 | 53 | 32 | 69
Greenseeker 2 | 83 | 93 | 75 | 60 | 90

## Slide 18: Site Specific
Chart: Rossville Corn R1 33000 Plants/Acre
| 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116
ACS-470 | 0.76973 | 0.76405 | 0.75471 | 0.73767 | 0.74788 | 0.71847 | 0.72597 | 0.79342 | 0.73141 | 0.74253 | 0.76517 | 0.7687 | 0.77585 | 0.77565 | 0.73868 | 0.69166
Greenseeker 2 | 0.7609 | 0.75337 | 0.74114 | 0.73372 | 0.73485 | 0.71213 | 0.72106 | 0.78909 | 0.73628 | 0.73899 | 0.75596 | 0.76205 | 0.76635 | 0.76741 | 0.73239 | 0.69898
Greenseeker Handheld | 0.73 | 0.83 | 0.82 | 0.74 | 0.81 | 0.82 | 0.8 | 0.76 | 0.8 | 0.8 | 0.8 | 0.67 | 0.76 | 0.8 | 0.79 | 0.82
Rapid Scan | 0.8046 | 0.7875 | 0.78 | 0.772 | 0.7786 | 0.7461 | 0.7622 | 0.8164 | 0.7779 | 0.7784 | 0.7982 | 0.7995 | 0.8072 | 0.7982 | 0.7667 | 0.7242
Within plot height variation caused significant issues with the data obtained with the Greenseeker Handheld due to a smaller working range for height. The Rossville site was on a deep sand soil but contained pockets of clay lenses which led to extreme height variation.

## Slide 19: Rossville Corn V10

## Slide 20
Chart: Rossville Corn R1 N Recommendations
| 106 | 107 | 111 | 112 | 115
ACS-470 | 94 | 86 | 46 | 46 | 77
Rapid Scan | 92 | 83 | 45 | 45 | 75
Greenseeker Handheld | 0 | 0 | 0 | 113 | 0
Greenseeker 2 | 102 | 102 | 57 | 57 | 86

## Slide 21: Field N Recommendation
Chart: lbs N/ac
| Rapid Scan | Greenseeker HH | Greenseeker 2 | ACS-470 | V10 | V10 | V10 | V10 | Sterling | Sterling | Sterling | Sterling
Bulk N Rec | 63.8 | 53 | 80.2 | 75.4
Std Dev | 12.0083 | 13.069 | 13.2552 | 18.0914
Chart: lbs N/ac
| Rapid Scan | Greenseeker HH | Greenseeker 2 | ACS-470 | R1 | R1 | R1 | R1 | Rossville | Rossville | Rossville | Rossville
Bulk N Rec | 68 | 22.6 | 80.8 | 69.8
Std Dev | 21.84 | 50.5 | 22.69 | 22.54

## Slide 22: Summary
The ACS-470 and Greenseeker 2 can use the same basic algorithm, but calibrating the algorithm for the sensor being utilized will likely improve the recommendations.
The Rapid Scan and Greenseeker Handheld will require calibration of an algorithm designed for the ACS-470 or Greenseeker 2.
The Greenseeker Handheld displays a tendency to give inconsistent data for corn sites with significant variability. Therefore we cannot recommend its use on corn at this time until this issue has been resolved.

## Slide 23: Continuing Research
Further research is needed in order to evaluate the site specific performance of these sensors and determine if sensor methods and settings need to be adjusted depending upon the crop condition, hybrid, populations, and current environmental conditions in order to optimize results for Variable Rate and Bulk field N applications.